## Slide 1
Neurophysiological techniques in animal models
Notes: Presentazione (Chi sono, come contattarmi)
Domande libere
Scopo della lezione -> capire meglio le tecniche che verranno usate nel resto del corso

## Slide 2
It is essential to have a toolbox of techniques to study the brain function
Motor output
Sensory input
Model of the world

## Slide 3
Electrophysiology
Imaging and light
Extracellular
  EEG (electroencephalography)
  LFP
    EP (evoked potentials)
  Single Units (“Spikes”)
Intracellular
  Patch Clamp
Intrinsic signal Optical Imaging (IOS)
Wide-field Calcium Imaging
2 Photon microscopy
Optogenetics

## Slide 4
Overview
IOS

## Slide 5
Electrophysiology
Imaging and light
Extracellular
  EEG (electroencephalography)
  LFP
    EP (evoked potentials)
  Single Units (“Spikes”)
Intracellular
  Patch Clamp
Intrinsic signal Optical Imaging (IOS)
Wide-field Calcium Imaging
2 Photon microscopy
Optogenetics

## Slide 6
Electrophysiology
In the nervous system, massive numbers of neurons constantly generate and transmit electrophysiological signals to communicate between neurons and brain regions.
The electrical nature of neurophysiology was first revealed by Italian scientist Luigi Galvani
In the last two centuries, neuroscientists detected neural activity from relatively large dissected nerves and axons, for example, the 0.5–1 mm-wide giant squid axons studied by Hodgkin and Huxley.
Pros | Cons
Measures directly electrical activity of neurons | Samples fewer neurons simultaneously
High temporal resolution (can detect single Action Potentials) | Overall more invasive for the brain tissue
Slightly overall lower cost | Hard or impossible to identify which neuron are we recording from
 | Trickier to record longitudinally from the same neurons

## Slide 7
The electrical activity of one or more neurons can be observed by recording voltage changes over time, thus producing a waveform that can be further analyzed
This kind of signal is surprisingly similar to what can be recorded by placing a microphone in front of a group of people talking. In this case the signal represent the oscillations in voltage produced in the microphone by the changes in air pressure (sound), but the core characteristics of the signal are closely related
This analogy (highlighted in red throughout the lecture) will be didactically useful to make some concepts more intuitive, however as with all the analogies, there are limitations (It’s an analogy, treat it like so)
The sound-electricity analogy

## Slide 8
Electrophysiology
Imaging and light
Extracellular
  EEG (electroencephalography)
  LFP
    EP (evoked potentials)
  Single Units (“Spikes”)
Intracellular
  Patch Clamp
Intrinsic signal Optical Imaging (IOS)
Wide-field Calcium Imaging
2 Photon microscopy
Optogenetics

## Slide 9
Extracellular Electrophysiology
Extracellular electrophysiology techniques measure neurophysiological signals by using a probe that records the voltage changes of the extracellular space.
The ionic movements underlying synaptic potentials (EPSPs and IPSPs) and action potentials generate a voltage change also in the extracellular space.
Since the probe is extracellular, we don’t have a precise idea of which cell is responsible for the signal that we are recording. We don’t know who are we listening to.
In this situation we can either decide to record the integrated activity of a group of numerous neurons, thus recording a population activity, or to employ some smart tricks to try to distinguish between different single neurons.
Imagine to be in a room full of people and recording the sound. You can either decide to listen to the general buzzing sound of the crowd, or you can try really hard to distinguish the voice of a single person in the room.

## Slide 10
Extracellular Electrophysiology
The broadband neural signals recorded from the extracellular space by either penetrating depth electrodes or surface electrodes can be processed to extract signals in different frequency bands, enabling the detection of at least two different types of voltage signals
  Slow-varying potentials (EEG and LFPs), which reflect collective transmembrane currents from multiple neurons;
  Action potentials, which last on the order of milliseconds (‘spikes’), from individual neurons or single units.

## Slide 11
EEG - Electroencephalography
The electroencephalogram (EEG) is a recording of the electric potentials measured most commonly from the scalp in humans and from the skull in model animals
The EEG is one of the oldest and most widely used methods for the investigation of the electric activity of the brain.
it has little discernible relationship with the firing patterns of the contributing individual neurons
Common uses of EEG
Detect different states of consciousness
Identify distinct sleep stages (REM vs non REM)
Detect the depth of anesthesia
Check connections and correlation between different areas of the cortex
Detect epileptic seizures

## Slide 12
The origin of the EEG signal
The EEG arises from synchronized synaptic activity in populations of cortical neurons.
Excitation of postsynaptic neurons creates an extracellular negative voltage on the dendrites as opposed to other parts of the neuron. This situation is referred to as a dipole: a region of positive charge separated from a region of negative charge by some distance.
The EEG signal detection is limited by the size of the electric field produced by a set of neurons. It needs to be large enough to be measurable at the surface. (Capacitive vs Volume conduction)
A single neuron’s dipole is too small to be measured at the scalp. However, because electrodes detect the sum of charges in their vicinity, the dipoles from multiple neurons in a region will sum together
Because electrodes will measure the sum of both the positive and the negative ends of dipoles in the brain, in order to produce a measurable (nonzero) signal, neurons must be both arranged in a parallel fashion, and synchronously active
Notes: A single neuron’s dipole is too small to be measured as far away as the scalp. However, because electrodes detect the sum of charges in their vicinity, the dipoles from multiple neurons in a region will sum together. The sum of many individual dipoles in an area is measurable as a single dipole whose magnitude reflects the number of neurons whose dipoles are summing together (Dugdale, 1993; Kandel et al., 2000). However, because electrodes will measure the sum of both the positive and the negative ends of dipoles in the brain, in order to produce a measurable (nonzero) signal, neurons must be both (a) arranged in a parallel fashion, and (b) synchronously active (Figure 2).
The parallel arrangement is necessary to produce a measurable dipole because, if the neurons are all arrayed in the same orientation, then their signals can sum to form a larger signal. In any other configuration, the individual dipoles’ positive and negative ends will sum and cancel each other out. The synchronization of activity is necessary in order to yield (a) a net charge on the scalp-facing side of the dipole sheet, rather than charges cancelling each other out; and (b) a signal large enough to be measured

## Slide 13
EEG for epilepsy
The EEG is the defining study for epilepsy and is used to support the diagnosis and the study of epilepsy both in humans and in model animals
Notes: EEG recordings from epileptic animals. A: Baseline EEG activity. B: A typical seizure event in an epileptic animal. This seizure was associated with behavioral rearing and loss of postural control (falling). C: An example of epileptiform activity recorded from an epileptic animal. The EEG segments shown below B and C are expansions of the periods marked by the solid bars. Animals were typically motionless or exhibited myoclonic jerks during epileptiform events. doi:10.1371/journal.pone.0046044.g001

## Slide 14
LFP - Local Field Potentials
LFPs differ from the EEG, in that LFPs are recorded in depth, from within the cortical tissue (or other deep brain structures) with microelectrodes. LFPs refer to the electric potential in the extracellular space around neurons.
LFPs sample relatively localized populations of neurons (100um-1mm). In contrast, the EEG samples much larger populations. For this reason LFP can be used to dissect activity in areas of the brain closer to each other (e.g., layers of the cortex)
Even if recorded close to the neuronal sources, LFP signals are also filtered, because the recording electrode is separated from the sources by portions of cortical tissue.
Besides these differences, EEG and LFP signals display analogous types of oscillations during wake and sleep states.
Notes: LFPs have a critical role in coordinating the activity of different regions of the brain, and synchronizing the activity of individual neurons with that of a neural network, through phase locking to the global rhythm10. For example, theta-frequency (4–8 Hz) oscillations and phase-locked discharge of neurons to theta waves are found in the hippocampus and some cortical areas, providing potential mechanisms to synchronize neuronal assemblies involved in complex processes and functions of the brain, such as memory formation and neuroplasticity

## Slide 15
Evoked Potentials
Evoked potentials are an electrical potential recorded from a specific part of the nervous system, especially the brain, following presentation of a stimulus such as a light flash or a pure tone.
EP can be recorded by measuring either EEG or LFP signal
EP amplitudes tend to be low (<1uV to several uV), compared to tens of microvolts for EEG, and often close to 20 millivolts for ECG. To resolve these low-amplitude potentials against the background of ongoing EEG, ECG, EMG, and ambient noise, signal averaging is usually required.
The signal is time-locked to the stimulus and most of the noise occurs randomly, allowing the noise to be averaged out with averaging of repeated responses.
A common type of evoked potential often measured in animals and humans are Visually Evoked Potentials (VEP) that are signal evoked in the visual part of the cortex after the presentation of a visual stimulus

## Slide 16
VEP to study animal models
EP (in this case VEP) can be used to probe the function of a specific part of the brain to search for abnormalities and, possibly, for biomarkers of a disease.
Since a large portion of the neural circuitry is shared between mice and humans, findings in animal models of a disease can be extrapolated to search for the same markers in humans

## Slide 17
Single Units (aka “Spikes”)
Individual neurons represent the structural and functional units of the nervous system,
Single-unit spikes are filtered from neural signals in the high-frequency spectrum (>250 Hz).
Importantly, extracellular electrodes provide information distinct from that of intracellular patch clamp recordings from single neurons: extracellular electrodes can record spiking from multiple nearby neurons (usually within a distance of ~140µm).
Spikes recorded at the same electrode can be temporally resolved and assigned to individual neurons with a procedure called spike sorting.
When spiking activity from multiple neurons cannot be resolved for assignment to individual neurons, it is usually referred to as multi-unit activity (MUA).

## Slide 18
Spike Sorting
It is already well established that complex brain processes are reflected by the activity of large neural populations and that the study of single-cells in isolation gives only a very limited view of the whole picture.
Spike sorting is of a critical importance, since it can allow the simultaneous analysis of the activity of a few individual close-by neurons from each recording electrode.
Spike sorting is the grouping of spikes into clusters based on the similarity of their shapes. Given that, in principle, each neuron tends to fire spikes of a particular shape, the resulting clusters correspond to the activity of different putative neurons. The end result of spike sorting is the determination of which spike corresponds to which of these neurons.
Oversampling recording electrodes such as tetrodes and high-density Michigan-type silicon probes further facilitate spike separation and assignment to individual neurons. Thus, single-unit signals generated by different neurons can be temporally resolved and, on the basis of the distinct amplitudes and waveforms of action potentials, the identity of each putative neuron can be discerned

## Slide 19
Extracellular traces using different recording methods are fundamentally similar
A 6s epoch of slow waves
scalp EEG (Cz, red), and LFP (blue) recorded by depth electrodes placed in the deep layers of the
  supplementary motor area (SM)
  entorhinal cortex (EC)
  hippocampus (HC)
  amygdala (Am)
Also shown are multiple-unit activity (MUA) (green) and spikes of isolated neurons (black ticks).

## Slide 20
Electrophysiology
Imaging and light
Extracellular
  EEG (electroencephalography)
  LFP
    EP (evoked potentials)
  Single Units (“Spikes”)
Intracellular
  Patch Clamp
Intrinsic signal Optical Imaging (IOS)
Wide-field Calcium Imaging
2 Photon microscopy
Optogenetics

## Slide 21
Intracellular Electrophysiology
Patch Clamp
Extracellular electrophysiology techniques measure neurophysiological signals by using a probe that records the voltage changes of the intracellular space.
These kind of recordings are usually done using micropipettes with very fine tips, size comparable to a dendrite.
We can obtain very thorough information of a very limited number of cells (in most cases only one) for each experiment.
Patch clamp is used to study ionic currents in individual isolated neurons, or patches of cell membrane.
Patch clamping can be performed in voltage clamp or in current clamp mode.
Notes: Fig. 6 Whole-cell patch clamp recordings from an LPeD1 neuron cultured on-chip. (a) Voltage responses (top) of an LPeD1 neuron to graded series of intracellular current pulses (bottom), after the rupture of the patch membrane and the attainment of the whole-cell configuration. The two upper curves were shifted up for clarity.

## Slide 22
Electrophysiology
Imaging and light
Extracellular
  EEG (electroencephalography)
  LFP
    EP (evoked potentials)
  Single Units (“Spikes”)
Intracellular
  Patch Clamp
Intrinsic signal Optical Imaging (IOS)
Wide-field Calcium Imaging
2 Photon microscopy
Optogenetics

## Slide 23
Imaging and light
Why should we use light to study the brain?
Light is an orthogonal stimulus for the vast majority of the brain tissue
By forming an image of the neural tissue of interest it is possible to actually see the neurons that we are recording from and select specific regions instead of recording electrical signals blindly
Pros | Cons
Samples many neurons simultaneously | Often measures optical phenomena that are correlated to electrical activity
Overall much less invasive for the brain tissue | Lower temporal resolution (almost impossible to detect single Action Potentials)
Easy to identify which neuron are we recording from | Overall higher cost
Easy to record longitudinally from the same neurons | Hard to record from deep areas of the brain

## Slide 24
Intrinsic Signal Optical Imaging (IOS)
Active areas of the brain consume more energy
In order for the ATP to be reconstituted, neurons need oxygen to sustain the oxidative metabolism
After a period of intense activity in an area of the brain there is a local and temporary depletion of oxygenated hemoglobin and a temporary increase in blood flow (neurovascular coupling)
Oxygenated and deoxygenated form of hemoglobin have different optical properties
We can use this local change in optical absorption to infer the underlying electrical activity
Tis signal is INTRINSIC. All animals (us included) have it

## Slide 25
Intrinsic Signal Optical Imaging
The technique employs appropriate sensory stimuli to obtain high resolution functional maps from a relatively large area.
Think of it like an optical version of an Evoked Potential
Optical imaging is probably the technique that best combines spatial resolution, coverage, speed and cost effectiveness for functional mapping of the mammalian cortex.
However, it has a very low temporal resolution

## Slide 26
IOS Imaging to study animal models
Much like with the VEP, Intrinsic Signal recordings of evoked activity can be used to search for abnormalities in the function of a brain region in a mouse model.
IOS it’s also very useful to locate spatially areas of the cortex functionally distinct

## Slide 27
Electrophysiology
Imaging and light
Extracellular
  EEG (electroencephalography)
  LFP
    EP (evoked potentials)
  Single Units (“Spikes”)
Intracellular
  Patch Clamp
Intrinsic signal Optical Imaging (IOS)
Wide-field Calcium Imaging
2 Photon microscopy
Optogenetics

## Slide 28
Calcium Imaging
An influx of calcium in the cell is correlated with electrical activity
  NMDA receptors
  Voltage gated Ca2+channels (soma and for vesicle release)
  Release from internal stores like the Endoplasmic Reticulum

## Slide 29
Calcium Imaging
Optical measurements of brain activity are attractive because they allow for simultaneous and noninvasive monitoring of activity from many individual neurons or from many different brain regions (population signals)
Since many years, calcium signals have been used as a correlate measure of action potentials in single cells and in brain areas.
The main advantages of Calcium Imaging are
  Very high signal-to-noise Ratio (indicators and Ca dynamics)
  The strong signal makes it possible to record in situation in which there is more background biological noise like in awake and behaving animals.
  Cell specificity with Genetically Encoded Calcium Indicators
There are some limitations to keep in mind:
  The relationship between action potentials and calcium may not be the same in all cells
  Many calcium indicators have nonlinearities resulting from high Hill coefficients
  Calcium dynamics are slow in contrast to voltage changes
  Hyperpolarization is likely to be missed by calcium indicators (caution to interpret negative calcium signals)

## Slide 30
Calcium Indicators

## Slide 31
Widefield Calcium Imaging
It is performed with a wide-field fluorescence microscope
It is limited to the superficial structures of the brain
Doesn’t have cellular resolution (but…)
It is possible to image up to the entire cortex simultaneously with a good spatial resolution. For this reason it is possible to discriminate the neural activity of different areas of the cortex and the flow of activity from one area to the other during a complex task
Can be performed in awake, behaving and even freely moving mice.

## Slide 32
Widefield Calcium Imaging
Can be used to identify specific properties of the visual cortex

## Slide 33
Can be used to detect activity in the motor cortex during the learning and execution of a specific motor task
Widefield Calcium Imaging

## Slide 34
Electrophysiology
Imaging and light
Extracellular
  EEG (electroencephalography)
  LFP
    EP (evoked potentials)
  Single Units (“Spikes”)
Intracellular
  Patch Clamp
Intrinsic signal Optical Imaging (IOS)
Wide-field Calcium Imaging
2 Photon microscopy
Optogenetics

## Slide 35
2-Photon microscopy
It is performed with a 2-photon LASER scanning microscope (TPLSM)
It is intrinsically CONFOCAL which means that the images are the result of optical sectioning of a single plane in the depth axis
It is limited to structures of the brain that are mostly superficial (up to 5-600um of depth), like the first layers of the cortex.
It’s possible to image deeper by using specific tricks (cannulas, prisms)
Is has cellular and even subcellular resolution
It is possible to image up to a large portion of the cortex simultaneously (it’s common to record the activity of 100-200 neurons at the same time)
Can be performed in awake and behaving mice (mostly head-fixed)

## Slide 36
2-Photon microscopy

## Slide 38
2-Photon microscopy
Can be used to record activity of single cells in an area of the cortex
The activity of cells can be correlated with a specific behavioral task of with a specific stimulus
It is possible to explore the connectivity of neurons with respect to their physical spatial location
Notes: Figure 8. Calcium Imaging in the Behaving Animal(A) Calcium imaging in the motor cortex of head-fixed mice engaged in an olfactory-related choice behavior with lick/no lick response. (Aa) Scheme of theexperimental set-up showing a head-fixed mouse under a two-photon microscope while performing the task. The task consists of the differentiation betweenodor A and B. The mouse is trained to lick only in response to one of the two odors. (Ab) Two-photon image of layer 2/3 cells. Left, overlay of sulforhodamine 101(SR101, red) and Oregon Green BAPTA-1 AM (green). Astrocytes are labeled by both dyes and thus appear yellow, whereas neurons are green. Right, regionsofinterest (ROI, green) overlaid on the Oregon Green BAPTA-1 channel. (Ac) Example of spontaneous calcium traces from ten neurons (black) and one astrocyte(gray). Panels (Ab) and (Ac) adapted by permission fromKomiyama et al. (2010).(B) Calcium imaging of place cells in the CA1 hippocampal region of mice which are placed on a spherical treadmill. (Ba) Experimental set-up: it consists ofa spherical treadmill, a virtual reality apparatus (with projector and surrounding screens) and a custom-made two-photon microscope. (Bb) Two-photon images ofneuron cell bodies in stratum pyramidale of CA1 labeled with the genetically encoded calcium indicator GCaMP3 (left). (Bc) Imaging CA1 place cells while themouse is running along a virtual linear track. Calcium traces are shown in black. The respective regions of interest are shown in (Bb), right panel. Red tracesindicate significant calcium transients. In parallel, the position of the mouse along the virtual linear track is recorded. Reward times are shown at the bottom. (Bd)Expanded view of the period indicated by the dashed box in (c). Panels (b)–(d) adapted by permission fromDombeck et al. (2010).876Neuron73, March 8, 2012ª2012 Elsevier Inc.NeuronPrimer

## Slide 39
Electrophysiology
Imaging and light
Extracellular
  EEG (electroencephalography)
  LFP
    EP (evoked potentials)
  Single Units (“Spikes”)
Intracellular
  Patch Clamp
Intrinsic signal Optical Imaging (IOS)
Wide-field Calcium Imaging
2 Photon microscopy
Optogenetics

## Slide 40
Optogenetics
Optogenetics is the combination of genetic and optical methods to cause or inhibit electrical events in specific cells of living tissue and behaving animals
It uses engineered version of light-sensitive bacterial proteins (Opsins). These proteins are mainly transmembrane channels that open in response to light of a specific wavelength.
The most common protein used is called ChannelRhodopsin and it activates a neuron when it’s activated by blue light
Many opsins are now available, varying in preferred wavelength and excitatory on inhibitory function

## Slide 41
Optogenetics
A variety of applications use optogenetic probes manipulate activity. Specificity can be achieved either by targeting probe expression to relevant cellular compartments or network elements or by targeting light to these elements.
The ability to implement optogenetics at different levels of nervous system function provides a powerful way to make causal links between these levels. (from correlation to causation – big breakthrough in neuroscience)
A key feature is the ability to target probes to genetically defined cell types and subcellular compartments, which allows the probes to be used for investigating multiple levels of nervous system function