## Slide 1
Dottorato in Ingegneria Industriale - Ciclo XXXV - Energetica e Tecnologie Industriali ed Ambientali Innovative
Candidate:
Alberto Amerini
Tutor: Coordinatore:
Prof. Bruno Facchini Prof. Giampaolo Manfrida
Co-Tutor:
Dott. Ing. Antonio Andreini
1st Year Presentation - 07/10/2020
Development of uncertainty quantification-based methodologies for robust design and optimization of high temperature components of turbomachines

## Slide 2: Uncertainty in turbomachinery
Numerical simulations in the turbomachinery area are often a deterministic exercise
Compressor blade
  A LE variation can produce a increase of pressure loss
  [A.P. Wheeler 2009]
  [R.S. Bunker 2009]
Combustor & HPT
  Geometric tolerance
  Boundary condition
  [C. Stimpson 2017]
Sand & Ice erosion:
  Clearence up to
  Tip chord reduced up to
  Pressure rise reduction
  [A. Ghenaiet 2005]

## Slide 3: Uncertainty Quantification
A set of methodologies that allow to quantify the propagation of uncertainty within numerical codes
The objective is the estimation of the PDF of the output quantities
UQ
Deterministic Approach
Probabilistic Approach

## Slide 4: Methodologies
Monte Carlo
Stochastic Methods
, for
  Polynomial chaos
    Total order
    Tensor quadrature (Gauss grid)
  Stochastic collocation
  Smolyak grid
  Curse of dimensionality
Polynomial coefficients
Polynomial basis functions

## Slide 5: Objectives and test case
Validation of UQ methods with DAKOTA
1D application Therm1D
3D application Film cooling performance
Test case

## Slide 6: Uncertain variables
 |  | Geo | HTC | BC | Overall
Monte Carlo |  | 10-100-1000 | 1000 | 1000 | 50-100-250-500-1000
Tensor/Stoch ord. 1 |  | 4 | 8 | 4 | 128
Tensor/Stoch ord. 2 |  | 9 |  |  | 
Tensor/Stoch ord. 3 |  | 16 |  |  | 
Tot ord.2 | c.r.=1 | 6 |  |  | 
 | c.r.=2 | 12 | 20 | 12 | 72
Tot ord.3 | c.r.=1 | 10 |  |  | 
 | c.r.=2 | 20 |  |  | 
Tot ord.4 | c.r.=2 | 30 |  |  | 
Smolyak level 1 |  |  |  |  | 15
Smolyak level 2 |  |  |  |  | 128
Smolyak level 3 |  |  |  |  | 807
Buondary conditions analysis
  Thermal quantities
  Kinematic quantities
HTC tuning factor analysis
Geometric analysis
  Angle
  Cd
Different types of analyses have been conducted
Overall analysis
  7 variables
  Smolyak grid validation
  Sensitivity analysis

## Slide 7: Interface script
An interface has been developed to allow DAKOTA to interact with Therm1D
A script has been written to process the output data
DAKOTA
Input File
Sampling
Therm-1D
Input File
Therm-1D
Therm-1D
Output File
Results
File
DAKOTA
Output File
Yes
No
Run
dprepro.py
Run
Read_Tw.py
DAKOTA
Interface
Python
Post process

## Slide 8: Results – Smolyak grid
TQ
TO
Sensitivity analysis
MC
SG
Maximum variability of 60%
Greater impact due to thermal quantities
Three variables have the greatest influence: , and
The output is dominated by the kinematic quantities

## Slide 9: Objectives and test case
Validation of UQ methods with DAKOTA
1D application Therm1D
3D application Film cooling performance
Additive Manufacturing
EDM
Numerical support for validation of experimental data
Uncertainty quantification analysis on a high fidelity CFD model
Show how geometric parameters affect the heat transfer
High temperatures reduce the integrity of turbine structural components.
Film cooling
Heat transfer measure:
Infrared thermography
Heat-mass anology:
PSP
(Pressure Sensitive Paint)
Adiabatic Effectiveness
ƞ

## Slide 10: Methodology – numerical setup
REDUCED GEOMETRY
RANS Approach
Turbolence model: k-ω SST
Second order discretization
: imposed pressure
Periodicity
Mesh | 
Full 3D | Reduced
20.5M | 3M
Film cooling on suction side only
Heat-mass transfer anology: mixture
FULL 3D
let
Chart: Time [h]
| Full 3D | Reduced
Mesh | 18 | 7

## Slide 11: Methodology - Geometry
Uncertain variables: angle, fillet radius and scale factor
Outputs: effectiveness on SS, BR and Cd
UQ analysis with tensor quadrature methology
  8 simulation needed
Parametric CAD to modify:
Angle of the hole
Blend radius
Hole scale
(1.)
Parameter | Range
Angle | 
Blend radius (r/D) | 1%
Scale factor | 0,9 1,1
Parameter | Range
Angle | 
Blend radius (r/D) | 
Scale factor | 
Methodology:
Geometry
Parameters
Mesh
Numerical Setup
Uncertainty
Quantification
{
Normal distribution
(3.)
(2.)

## Slide 12: Results - Adiabatic Effectiveness
GAUSS GRID |  | 
 | DP0 | DP7
ANGLE | -2,1991 | 2,1991°
BLEND RADIUS | 1,9445E-5 m | 4,055E-5 m
SCALE FACTOR | 0,956 | 1,044
GAUSS GRID |  | 
 | DP0 | DP7
ANGLE |  | 2,1991°
BLEND RADIUS | 1,9445E-5 m | 4,055E-5 m
SCALE FACTOR | 0,956 | 1,044
Uncertainty 
Uncertainty 
PDF
s
DP0
DP7
η
UQ analysis8 simulations required
  PCE method

## Slide 13: Results - Blowing Ratio & Cd
  Simulation without film cooling isentropic mach number
  Isentropic relations and perfect gases law

## Slide 14: Conclusions & Publications
DAKOTA has proved functional for 1D and 3D applications performed
Stochastic methods are efficient compared to Monte Carlo method
Sensitivity analysis determines the impact of uncertainties on the outputs through quantitative indices
Future works
  Apply UQ methods to other test cases
  Use DAKOTA for robust design and optimization applications
  Development of a standard procedure to use the results of the UQ analysis to update the design project
National conferences
  Gamannossi, A., Amerini, A., Poggiali, M., Elmi, C. A., Mazzei, L., & Andreini, A. (2019, December). Uncertainty quantification of an aeronautical combustor using a 1-D approach. ATI 2019 In AIP Conference Proceedings (Vol. 2191, No. 1, p. 020083). AIP Publishing LLC.
  Poggiali, M., Gamannossi, A., Langone, L., & Amerini, A. (2019, December). Civil aero-engine performance prediction using a low-order code and uncertainty quantification estimation. ATI 2019. In AIP Conference Proceedings (Vol. 2191, No. 1, p. 020130). AIP Publishing LLC.
International conferences
  Gamannossi, A., Amerini, A., Poggiali, M., Elmi, C. A., Mazzei, L., & Andreini, A. “Application of uncertainty quantification methods to the prediction of effusion cooled combustor liner temperature”. ASME Turbo Expo 2020 Turbomachinery Technical Conference and Exposition GT2020 September 2020
International journals
  Gamannossi, A., Amerini, A., Mazzei, L., Bacci, T., Poggiali, M., & Andreini, A. (2020). Uncertainty Quantification of Film Cooling Performance of an Industrial Gas Turbine Vane. Entropy, 22(1), 16.

## Slide 15
Dottorato in Ingegneria Industriale - Ciclo XXXV - Energetica e Tecnologie Industriali ed Ambientali Innovative
Candidate:
Alberto Amerini
Tutor: Coordinatore:
Prof. Bruno Facchini Prof. Giampaolo Manfrida
Co-Tutor:
Dott. Ing. Antonio Andreini
1st Year Presentation - 07/10/2020
Development of uncertainty quantification-based methodologies for robust design and optimization of high temperature components of turbomachines